## Slide 1
© Philip Kolb
Slide number 01
The basics of “MacCready flying”

## Slide 2: Paul B. MacCready (1925-2007)
© Philip Kolb
Slide number 02

## Slide 3: Paul B. MacCready (September 25, 1925 – August 28, 2007)
© Philip Kolb
Slide number 03
was an American aeronautical engineer.
He was the founder of AeroVironment and devoted his life to developing more efficient transportation vehicles that could "do more with less".
With Dr. Peter B.S. Lissaman, he created a human-powered aircraft, the Gossamer Condor.
The Condor stayed aloft for seven minutes while it completed a figure eight course, thereby winning the first Kremer prize in August 1977.
The award winning plane was constructed of aluminum tubing, foam, piano wire, bicycle parts and mylar foil.
He later created solar-powered aircraft also, f.e. the Gossamer Penguin and Solar Challenger.
He was involved in the development of NASA's solar-powered flying wings such as the Helios, which surpassed the SR-71's altitude records and could theoretically fly on Mars (where the atmosphere is thin and has little oxygen).
But he also was a soaring pilot!!!

## Slide 4: Paul B. MacCready (September 25, 1925 – August 28, 2007)
© Philip Kolb
Slide number 04
Paul MacCready was also a devoted glider pilot and won the U.S. National Open Class Soaring Championship 3 times (1948, 1949, 1953).
In 1956, he became the first American pilot to become the World Soaring Champion.

## Slide 5: Paul B. MacCready (September 25, 1925 – August 28, 2007)
© Philip Kolb
Slide number 05
Since around 1947 MacCready was working on a way to select the optimum airspeed to maximize his “Cross Country Speed”.
To achieve this he was using the airplanes polar to calculate the “Speed to Fly”.
Paul Mac Cready therefore is renown as the "inventor" of the "Speed To Fly"-theory.
In essence, this theory is quite simple: → When the lift ahead promises to be strong you should fly faster.
→ When the lift ahead looks to be weaker, you should fly closer to your glider’s best L/D speed.
MC theory tells you exactly how fast you should fly based on the strength of lift you expect ahead.

## Slide 6
© Philip Kolb
Slide number 06
„The POLAR“
YES!!! We remember that!!!

## Slide 7
© Philip Kolb
Slide number 07
„Sink-Polar“ (Air Speed vs. Sink Speed)
And we remember that the tangent out of the point of origin “touching” the polar curve reflects the maximum L/D!

## Slide 8
© Philip Kolb
Slide number 08
„Sink-Polar“ (Air Speed vs. Sink Speed)
As well as the “Speed to Fly” to achieve the maximum L/D.

## Slide 9
© Philip Kolb
Slide number 09
Ahhh!!!!
So the “Speed to Fly” for reaching the farthest possible distance,
is the speed indicated for the maximum L/D for my glider!
But only in “still” or “dead” air!!!

## Slide 10
© Philip Kolb
Slide number 10
„Sink-Polar“ (Air Speed vs. Sink Speed)
In “still” or “dead” air we remember, that we can glide for about 39,74km
out of 1000m of altitude.

## Slide 11
© Philip Kolb
Slide number 11
In “still” or “dead” air we remember, that we can glide for about 39,74km
out of 1000m of altitude.
„Glide-Polar“ (L/D vs. Air Speed)
Maximum L/D about 39,74 @ 15,5m/s airspeed

## Slide 12
© Philip Kolb
Slide number 12
„Sink-Polar“ (Air Speed vs. Sink Speed)
In “still” or “dead” air we remember, that we can glide for about 39,74km
out of 1000m of altitude.
What would happen if we encounter a strong headwind? …let`s say 15,5m/s headwind???
How far could we go then?

## Slide 13
© Philip Kolb
Slide number 13
„Glide-Polar“ (L/D vs. Air Speed)
Maximum L/D about 39,74 @ 15,5m/s airspeed
@ 15,5m/s headwind
and 15,5m/s airspeed
= 0 !!!
Both velocities cancel out and we would glide at best L/D “standing still” over the ground!

## Slide 14
© Philip Kolb
Slide number 14
„Glide-Polar“ (L/D vs. Air Speed)
Maximum L/D about 39,74 @ 15,5m/s airspeed
@ 15,5m/s headwind
and 15,5m/s airspeed
To cover ground into a head wind, we need to push up the speed!!!
But this will come at a cost!
Our L/D is going down!

## Slide 15
© Philip Kolb
Slide number 15
So to cover ground into a headwind, we need to push up the speed!
But by how much?
And what will be the best L/D at a given Headwind? What will be the necessary “Speed to Fly”?

## Slide 16
© Philip Kolb
Slide number 16
„Sink-Polar“ (Air Speed vs. Sink Speed)
In “still” or “dead” air we remember, that we can glide for about 39,74km
out of 1000m of altitude.
Now we head into 7m/s wind
So we put the origin of our tangent in +7.0 on the X-Axis and touch the polar!
Best L/D for 7m/s headwind
@ 18,8m/s airspeed

## Slide 17
© Philip Kolb
Slide number 17
„Sink-Polar“ (Air Speed vs. Sink Speed)
Best L/D for 7m/s headwind
@ 18,8m/s airspeed
Groundspeed = 11,8m/s
Sink speed = 0,5m/s
Best L/D for 7m/s Headwind = 23,6

## Slide 18
© Philip Kolb
Slide number 18
„Sink-Polar“ (Air Speed vs. Sink Speed)
The “Speed to Fly” into a 15,5m/s headwind is 26.6m/s air speed!
Ground speed = 11,1m/s
Sink speed = 1m/s
The maximum L/D at the “Speed to Fly” for 15,5m/s headwind is 11.1!

## Slide 19
© Philip Kolb
Slide number 19
Luckily there isn't always a headwind to fly into!
To find the best “Speed to Fly” for a tailwind situation works just the same!

## Slide 20
© Philip Kolb
Slide number 20
„Sink-Polar“ (Air Speed vs. Sink Speed)
Best L/D for 7m/s tailwind @13,5m/s airspeed
Let’s say we are flying down the course with a 7m/s tailwind!
In this case we will set the origin of the tangent touching our polar at “-7,0” on the X-Axis

## Slide 21
© Philip Kolb
Slide number 21
„Sink-Polar“ (Air Speed vs. Sink Speed)
Best L/D for 7m/s tailwind @13,5m/s airspeed
Groundspeed = 20,5m/s
Sink speed = 0,37m/s
The maximum L/D at the “Speed to Fly” for 7m/s tailwind is 55.4!

## Slide 22
© Philip Kolb
Slide number 22
„Sink-Polar“ (Air Speed vs. Sink Speed)
Different “Speed to Fly” for different head- or tailwind components to achieve the best L/D for each scenario.

## Slide 23
© Philip Kolb
Slide number 23
We can slow down the plane in a tailwind situation!
But we need to speed up the plane in a headwind situation! …for achieving the best possible L/D.

## Slide 24
© Philip Kolb
Slide number 24
Now what would happen, if there’s not only wind but Thermals?
Updrafts
and
Sink

## Slide 25
© Philip Kolb
Slide number 25
In the case of vertical movements of the air – like thermals and sink – the vertical axis (Y-Axis) get’s important!
„Sink-Polar“ (Air Speed vs. Sink Speed)

## Slide 26
© Philip Kolb
Slide number 26
„Sink-Polar“ (Air Speed vs. Sink Speed)
How fast to fly, when we encounter a soft (weak) thermal? Let’s say it just offers 0,33m/s climb rate…
Best L/D @ 12.7m/s
air speed
In this special case the tangent touching the polar is parallel to the X-Axis.
The velocity of the rising air mass cancels out the sink rate of the aircraft and thus we could fly on and on …and on…and on….
L/D = ∞

## Slide 27
© Philip Kolb
Slide number 27
As this is a very theoretical but unrealistic scenario. Let’s see what speed we need to fly when encountering sink
f.e. after thermaling in lift.

## Slide 28
© Philip Kolb
Slide number 28
After leaving the thermal we encounter 1,6m/s sink.
„Sink-Polar“ (Air Speed vs. Sink Speed)
Best L/D for 1,6m/s sink. “Speed to Fly” = 28,0 m/s air speed!

## Slide 29
© Philip Kolb
Slide number 29
No matter what! We´re gonna push through that nasty sink!!!
„Sink-Polar“ (Air Speed vs. Sink Speed)
Groundspeed = 28m/s
Sink speed = - 2,72m/s
Sink rate of the air mass (= -1,6m/s)
and the sink rate of the aircraft (-1,12m/s)
add up!
….even if it will be at the cost of a best possible L/D of 10.3!

## Slide 30
© Philip Kolb
Slide number 30
We can slow down the plane if we fly straight line through a thermal!
We can`t help it! We need to push through the sink. …for achieving the best possible L/D.

## Slide 31
© Philip Kolb
Slide number 31
For understanding the “Speed to Fly” criteria, we need an understanding of the polar of our glider and the air mass we are flying through!
„Sink-Polar“ (Air Speed vs. Sink Speed)
Best L/D = 8,6 for 6m/s headwind and 1,5m/s sink “Speed to Fly” = 30m/s
Best L/D = 25,5 for 7m/s tailwind and 0,5m/s sink “Speed to Fly” = 17,2m/s
Best L/D = 115 for 2m/s headwind and 0,25m/s climb “Speed to Fly” = 13m/s
Best L/D = - 37,2 ( “-”!!!) for 4m/s tailwind and 1,4m/s climb “Speed to Fly” = 10,5m/s
This reflects a very special case where “dolphin-style” flying could be chosen. If the conditions hold up, our aircraft can climb the most and fly the farthest at the same time. In this case climb 1000m while covering 37,2km distance.

## Slide 32
© Philip Kolb
Slide number 32
Camber / Reflex setup as a possible way to tweak our planes´ performance!
We remember this!!!

## Slide 33
© Philip Kolb
Slide number 33

## Slide 34
© Philip Kolb
Slide number 34
„Sink-Polar“ (Air Speed vs. Sink Speed)
Best L/D = 115 for 2m/s headwind and 0,25m/s climb “Speed to Fly” = 13m/s
Adapting our aircrafts configuration in accordance to the necessary “Speed to Fly”
Polar for f = 0 degrees
Best L/D = 155 for 2m/s headwind and 0,25m/s climb “Speed to Fly” = 12,7m/s
Polar for f = +5 degrees

## Slide 35
© Philip Kolb
Slide number 35
Now we know the basics of MacCready-Flying.
And yes….. We need to know about our planes’ polar!
The more accurate this knowledge is,
the better we can adapt our flying.
Nevertheless… It is better to understand this concept first, than knowing the exact numbers.
Because this knowledge
- and as well some flight testing – can lead us towards making the right Assumptions!

## Slide 36
© Philip Kolb
Slide number 36
Assumptions
That’s what the Classic MacCready Theory is based upon: Assumptions
made out of
knowledge and experience!
What would you assume for your flight tactics when looking at this
“cloud-street”?

## Slide 37
© Philip Kolb
Slide number 37
If we can make the right assumptions,
the concept of the “Speed to fly” theory can not only get us fly longer distances, it also can get us to cover ground faster!

## Slide 38
© Philip Kolb
Slide number 38
It is all about the best possible educated guess (assumption) of the thermal strength of:
The next thermal ahead
The next thermals ahead
The thermals (ahead) in general
What if someone could tell us
the strength of that thermal?
Is it
1m/s
2m/s
3m/s
…???
What would we do with
that information?

## Slide 39
© Philip Kolb
Slide number 39
Let’s say the thermal ahead offers a 2m/s average climb in reality.
2m/s
Pilot B is careful. He assumes the thermal ahead offers 1m/s climb. He is not pushing very hard and takes a lot of time to reach the thermal. He reaches it in good altitude – but late.
Pilot C is aggressive. He assumes the thermal ahead offers 3m/s climb. He is pushing very hard and takes a lot of risk “driving almost into the ground”.
He is the first to reaches it – but low…and needs to spend a lot of time climbing back up!

## Slide 40
© Philip Kolb
Slide number 40
Let’s say the thermal ahead offers a 2m/s average climb in reality.
2m/s
Pilot A chooses the right “Speed to Fly”. He assumes the thermal ahead offers 2m/s climb. He reaches it in reasonable altitude and can climb his way back to resume flying on course first. He will gain valuable speed over the other two pilots.

## Slide 41
© Philip Kolb
Slide number 41
„Sink-Polar“ (Air Speed vs. Sink Speed)
If we assume the next thermal(s) will offer 1,5m/s climb rate…
… we need to push forward in between thermals with the same
“Speed to Fly” as if we would push through 1,5m/s sink!
26,4m/s

## Slide 42
© Philip Kolb
Slide number 42
„Sink-Polar“ (Air Speed vs. Sink Speed)
If our assumptions are right,
We can reach the next thermal(s) and the air in between thermal(s) is “calm”,
our effective average cross country speed will be…
26,4m/s
16,7m/s
We can read it out at the intersection, where our tangent is crossing the X-Axis.

## Slide 43
© Philip Kolb
Slide number 43
This is actually what the “classic” MacCready-theory is about.
It is about assuming and calculating the best “Speed to Fly” to predict the best possible cross country speed.

## Slide 44
© Philip Kolb
Slide number 44
And it works for us as well!
Teaching us to make assumptions about the weather conditions and thermal strength.
Knowing about the basic principles of performance polars.
Avoiding mistakes.
Knowing when to take risks and when to be careful.
Supporting our tactical approach.

## Slide 45
© Philip Kolb
Slide number 45
Pilot B is reaching a much higher average speed!

## Slide 46
© Philip Kolb
Slide number 46
A final example of making good use of the MacCready-theory

## Slide 47
© Philip Kolb
Slide number 47
Summary and “lessons learned”
What of all this can we take to the field?
Know the limitations of the model you apply!
Precise assuming and setting of the MacCready values is not extremely important! Just try and avoid huge mistakes!
Conservative MacCready flying increase your chances of finding (better) lift!
Aggressive MacCready flying can win you a round! But can also increase the chance of landing way too early!
Fly aggressive and push up the speed when you are high. Don’t circle in weak lift, take only the strong thermals!
Fly conservative and careful when getting low. Choose not to push too hard and choose also weaker thermals to stay airborne.
Apply the laws and rules about basic MacCready flying and learn from it. Sharpen your perceptıons while applying it to be able to make better and better assumptions!
What else?

## Slide 48
© Philip Kolb
Slide number 48
Enough for now!!!
Thank you for your attention!
Let this sink in.
Any Questions?