## Slide 1
© Philip Kolb
Slide number 01
A little bit about model glider performance

## Slide 2
© Philip Kolb
Slide number 02
What is „performance“?
“This glider has an amazing performance!”
“This glider handles great!!!”
Difference!
Performance-Parameters like:
Maximum L/D (lift-to-drag-ratio)
Wide range of high L/D´s
Minimum sink
Handling-Parameters (flight mechanics) like:
Directional stability
Spiral stability
High “agility” (throw authority, low inertia)
“control harmony"
Note: A glider which “handles nice and easy”, gives us the possibility to get the maximum performance out of it!

## Slide 3: Let´s take a look and understand “performance”:
How can we describe the “performance” of our model gliders?
How can we compare the “performance” of our model gliders?
How can we get “performance” out of our gliders?
How can we tweak our models “performance”?
How can we avoid mistakes by knowing about our gliders performance?
© Philip Kolb
Slide number 03

## Slide 4
© Philip Kolb
Slide number 04
„The POLAR“

## Slide 5
© Philip Kolb
Slide number 05
„Sink-Polar“ (Air Speed vs. Sink Speed)
 That is what it`s all about!!! 

## Slide 6
© Philip Kolb
Slide number 06
„Sink-Polar“ (Air Speed vs. Sink Speed)

## Slide 7
© Philip Kolb
Slide number 07
„Sink-Polar“ (Air Speed vs. Sink Speed)
The tangent out of the point of origin “touching” the polar curve reflects the maximum glide ratio!

## Slide 8
© Philip Kolb
Slide number 08
„Sink-Polar“ (Air Speed vs. Sink Speed)
“Glide ratio” describes the ratio between Lift and Drag proportions on our aircraft.
→ Lift over Drag
→ Lift / Drag
→ L / D
In the case shown, the tangent touches the polar curve at an air speed of 15,5m/s. This reflects a sink speed of 0,39m/s.
Thus the maximum L/D ratio here is: 15,5m/s : 0,39m/s = 39,74

## Slide 9
© Philip Kolb
Slide number 09
Is there any other way to depict this?
Of course! Calculate a curve of all L/D-values over the air speed!

## Slide 10
© Philip Kolb
Slide number 10
„Glide-Polar“ (L/D vs. Air Speed)

## Slide 11
© Philip Kolb
Slide number 11
„Glide-Polar“ (L/D vs. Air Speed)
This curve reflects the glide ratios of our aircraft (in deed “only the wing”) at 7kg AUW and flaps in “Zero-degree-position”.

## Slide 12
© Philip Kolb
Slide number 12
„Glide-Polar“ (L/D vs. Air Speed)
This curve reflects the glide ratios of our aircraft (in deed “only the wing”) at 7kg AUW and flaps in “Zero-degree-position”.
Maximum L/D about 39,74 @ 15,5m/s airspeed
…just like we`ve calculated before…
Going faster than that means, that L/D values drop. But you can be “somewhere” earlier. …even if this might mean “on the ground”!
Going slower than that means, that L/D values drop. You might not be able to reach your goal anymore, but stay in the air longer!

## Slide 13
© Philip Kolb
Slide number 13
L/D as a determining number for our planes´ performance!
What else?

## Slide 14
© Philip Kolb
Slide number 14
„Sink-Polar“ (Air Speed vs. Sink Speed)
Besides L/D we can measure performance of our gliders by it´s minimum sink rate. Both items are not necessarily the same!
In this case the minimum sink rate of this gliders wing at 7kg AUW with its flap in “zero position” is about 0,33m/s.
Flying at minimum sink will keep us aloft for the longest possible time in “dead air”. The air speed for min. sink in this case is 12,7m/s, which is considerably lower than the speed for best L/D.

## Slide 15
© Philip Kolb
Slide number 15
„Endurance-Polar“ (L^(3/2)/D vs. Air Speed)

## Slide 16
© Philip Kolb
Slide number 16
„Endurance-Polar“ (L^(3/2)/D vs. Air Speed)
As noticed from the Sink-Polars, the air speed for minimum sink is readable from this polar as well. It reaches its maximum endurance parameter at an airspeed of 12,7m/s.

## Slide 17
© Philip Kolb
Slide number 17
So how to tweak the setup of our aircraft
by considering these polars?!

## Slide 18
© Philip Kolb
Slide number 18

## Slide 19
© Philip Kolb
Slide number 19
Green polar: Aircrafts wing at 7kg AUW with flaps in “zero position” (f00)
Yellow polar: Aircrafts wing at 7kg AUW with flaps set to 2 degrees camber (f20)
„Sink-Polar“ (Air Speed vs. Sink Speed)

## Slide 20
© Philip Kolb
Slide number 20
Green polar: Aircrafts wing at 7kg AUW with flaps in “zero position” (f00)
Yellow polar: Aircrafts wing at 7kg AUW with flaps set to 2 degrees camber (f20)
„Glide-Polar“ (L/D vs. Air Speed)
The pilot should switch flight-modes at about 20m/s air speed!
Faster than 20m/s → flaps 0 degrees
Slower than 20m/s → flaps +2 degrees

## Slide 21
© Philip Kolb
Slide number 21
Green polar: Aircrafts wing at 7kg AUW with flaps in “zero position” (f00)
Yellow polar: Aircrafts wing at 7kg AUW with flaps set to 2 degrees camber (f20)
„Sink-Polar“ (Air Speed vs. Sink Speed)
Blue polar: Aircrafts wing at 7kg AUW with flaps set to -1 degrees reflex (f-10)

## Slide 22
© Philip Kolb
Slide number 22
Green polar: Aircrafts wing at 7kg AUW with flaps in “zero position” (f00)
Yellow polar: Aircrafts wing at 7kg AUW with flaps set to 2 degrees camber (f20)
„Glide-Polar“ (L/D vs. Air Speed)
Blue polar: Aircrafts wing at 7kg AUW with flaps set to -1 degrees reflex (f-10)
Now search the shifting points for the flight-mode switches!!!

## Slide 23
© Philip Kolb
Slide number 23
Camber / Reflex setup as a possible way to tweak our planes´ performance!
What else?

## Slide 24
© Philip Kolb
Slide number 24
What else?

## Slide 25
© Philip Kolb
Slide number 25
How to quantify the effects of ballast???

## Slide 26
© Philip Kolb
Slide number 26
Green polar: Aircrafts wing at 7kg AUW with flaps in “zero position” (f00)
Yellow polar: Aircrafts wing at 7kg AUW with flaps set to 2 degrees camber (f20)
„Sink-Polar“ (Air Speed vs. Sink Speed)
Blue polar: Aircrafts wing at 7kg AUW with flaps set to -1 degrees reflex (f-10)
What would happen if we add another 2kg of ballast to the “f00-glider” (green polar)???

## Slide 27
© Philip Kolb
Slide number 27
Green polar: Aircrafts wing at 7kg AUW with flaps in “zero position” (f00)
Yellow polar: Aircrafts wing at 7kg AUW with flaps set to 2 degrees camber (f20)
„Sink-Polar“ (Air Speed vs. Sink Speed)
Blue polar: Aircrafts wing at 7kg AUW with flaps set to -1 degrees reflex (f-10)
What would happen if we add another 2kg of ballast to the “f00-glider” (green polar)???

## Slide 28
© Philip Kolb
Slide number 28
Green polar: Aircrafts wing at 7kg AUW with flaps in “zero position” (f00)
Yellow polar: Aircrafts wing at 7kg AUW with flaps set to 2 degrees camber (f20)
„Glide-Polar“ (L/D vs. Air Speed)
Blue polar: Aircrafts wing at 7kg AUW with flaps set to -1 degrees reflex (f-10)
What would happen if we add another 2kg of ballast to the “f00-glider” (green polar)???
Adding ballast primarily is shifting our performance-polars to the right towards higher L/D-numbers at faster air speeds.
At the same time the stall speed and minimum sink is increasing which can harm performance at slow air speeds.

## Slide 29
© Philip Kolb
Slide number 29
Before trying to meticulously set Camber and Reflex the perfect way, try and think about ballasting first!
What else?

## Slide 30
© Philip Kolb
Slide number 30
Enough for now!!!
Thank you for your attention!
Let this sink in …..we`ll be back with the basics of “MacCready – Flying” soon.
Any Questions?